## Slide 1
S = 1151 mm
D = 200 mm
B = 100 mm
a = 100 mm
Notch width = 4 mm
TPB Test

## Slide 2
LDPM Part
Size in XYZ: 100mm x 100mm x 200mm
Generated using FreeCAD
Mesh information is stored in LDPM mesh folder
Folder:
LDPM mesh 8-16:
Minimum particle size is 8mm
Maximum particle size is 16mm
LDPM mesh 5-16:
Minimum particle size is 5mm
Maximum particle size is 16mm

## Slide 3
LDPM Part
Material Property:

## Slide 4
FEA Part (left and right)
Size in XYZ: 525.5mm x 100mm x 200mm
Mesh information is stored in FEA mesh.inp
Mesh type: C3D4
The left part and the right part have the same mesh
Material Property:
Young’s Modules E: 39000 MPa;
Poisson ratio v: 0.2
Density: 2.338E-9

## Slide 5
Steel Part (loading and supports)
Size in XYZ: 25mm x 100mm x 10mm
Mesh information is stored in Steel mesh.inp
Mesh type: C3D4
The loading and supports parts have the same mesh
Material Property:
Young’s Modules E: 20000 MPa;
Poisson ratio v: 0.3
Density: 7.8 E-9
Assumed as rigid body

## Slide 6
Tie
Tie
Tie
Tie